Vortex Pump XKFm

XKFm

Pump  
Peripheral pump
Liquid pumped temperature up to 60℃ 
Clean water, non-aggressive liquid

Specifications

| Model | Power | Inlet/Outlet | Max. Flow (L/min) | Max. Head (m) | Max. Suct (m) |
| --- | --- | --- | --- | --- | --- |
|  | (kW) | (HP) |  |  |  |  |
| XKFm/1 | 0.37 | 0.5 | 1″×1″ | 40 | 40 | 8 |

Hydraulic Performance Curve

Motor

Single phase/Three-phase, 50Hz/60Hz

Insulation class: 130
Protection class: IP44
Ambient temperature up to 40℃
With thermal overload protection
Copper winding

Parts Information of Vortex Pump

|  | Part | Material | Remark |
| --- | --- | --- | --- |
| 1 | Pump body | Cast iron | Electrophoretic treatment, ABS |
| 2 | Impeller | Brass |  |
| 3 | Mechanical seal | Silicon carbide/Graphite |  |
| 4 | Support | Cast iron | Electrophoretic treatment, ABS |
| 5 | Bearing | High quality |  |
| 6 | Rotor | Cold-rolled sheet | Welded stainless steel shaft |
| 7 | Stator | Aluminum casing | Cold-rolled sheet stator |
| 8 | End plate | Aluminum |  |
| 9 | Fan | Noryl |  |
| 10 | Fan cover | Iron |  |
| 11 | Capacitor | High quality |  |

LEO is a professional vortex pump manufacturer and supplier in China. Our peripheral pumps have passed the GS, CE, UL, ETL, CB, EMC and EMF certification, and are well accepted by customers in many countries, including the USA, Italy, Canada, Russia, France, Britain, India, Australia, just to name a few. We welcome both domestic and international customers to choose water pumps and garden machines, including submersible pumps, centrifugal pumps, garden shredders and snow throwers etc.