Vortex Pump XQm

XQm

Pump  
Peripheral pump
Liquid pumped temperature up to 60℃ 
Clean water, non-aggressive liquid 

Specifications

| Model | Power | Inlet/Outlet | Max. Flow (L/min) | Max. Head (m) | Max. Suct (m) |
| --- | --- | --- | --- | --- | --- |
|  | (kW) | (HP) |  |  |  |  |
| XQm60 | 0.37 | 0.5 | 1″×1″ | 40 | 40 | 8 |
| XQm70 | 0.6 | 0.8 | 1″×1″ | 50 | 65 | 8 |
| XQm80 | 0.75 | 1.0 | 1″×1″ | 60 | 70 | 8 |

Hydraulic Performance Curve

Motor 
Single phase/Three-phase, 50Hz/60Hz

Insulation class: 130
Protection class: IP44
Ambient temperature up to 40℃
With thermal overload protection
Copper winding

Parts Information of Vortex Pump

|  | Part | Material | Remark |
| --- | --- | --- | --- |
| 1 | Pump body | Cast iron | Electrophoretic treatment, ABS |
| 2 | Impeller | Brass |  |
| 3 | Mechanical seal | Silicon carbide/Graphite |  |
| 4 | Support | Cast iron | Electrophoretic treatment, ABS |
| 5 | Bearing | High quality |  |
| 6 | Rotor | Cold-rolled sheet | Welded stainless steel shaft |
| 7 | Stator | Aluminum casing | Cold-rolled sheet stator |
| 8 | End plate | Aluminum |  |
| 9 | Fan | Noryl |  |
| 10 | Fan cover | Iron |  |
| 11 | Capacitor | High quality |  |

As an acclaimed supplier of vortex pumps in China, LEO produces a wide range of water pumps and garden machines, including centrifugal pumps, submersible pumps, garden shredders, and lawn mowers etc. These products are made in accordance with GS, CE, UL, ETL, CB, EMC and EMF standards. Now they are extensively used in USA, Canada, Russia, France, Britain, India, Australia, Israel, Iraq, among others. 
For more detailed information, please contact us directly.